The Neutrino Factory, Muon Production and Acceleration

---
What is the Neutrino Factory?
- Produces a focussed beam of neutrinos from boosted muon decays
  - Energy in the region of 10s of GeV
- Baseline uses 25GeV muon parents
- Muons are made from pion decays
  - Must be accelerated fast from 100s of MeV
- Pions come from hadronic fragmentation of target nuclei bombarded by multi-GeV, multi-MW protons
LAS
Forward calorimeter

---
Why 10s of GeV Neutrinos?
- Puts the oscillation wavelength of neutrinos on the same scale as the Earth
  - Upper limit (barring space travel)
- Also we have some trouble detecting slower neutrinos
  - Lower limit
- Boost collimation vs. oscillation distance cancel, but detector cross-sections increase with energy

---
Example Detector Sensitivity
From current baseline document
ids-nf.org

---
Example Physics Sensitivity
From International Scoping Study (ISS) physics report
RAL technical reports 2007

---
Current “IDS” Baseline v1.0

---
R&D Projects in the NF Context
FETS
ISIS upgrades
Target studies
MICE
EMMA
Plus conceptual design group covering most areas and Ciprian Plostinar designing the proton linac

---
Target Studies at RAL
- Pulsed current wire test (video 1)
- Simulations
  - Pion production
  - Target (and wire) thermal shock
  - Mercury jet engineering issues (video 2)
  - Target station magnet forces
- Tungsten powder jet flow loop (video 3)
- Collaboration with MERIT

---
Muon Acceleration
Problem with secondary beams is that they are not well collimated (large emittance)

---
Muon Acceleration
- Problem with secondary beams is that they are not well collimated (large emittance)
  - Large RF aperture
- Muons also decay in 2.2 + 20.8(E/GeV) ms
  - 0.66 + 6.23(E/GeV) km/c
  - Need high gradient, can't rephase
- Fortunately we are slowing down time and compressing space as E increases!

---
“MICE” cavity 201MHz
42cm Ø 16;12MV/m (peak;avg.)
“ILC” cavity 1.3GHz
7cm Ø 59;31.5MV/m

---
Project X at Fermilab

---
Conclusion
- Neutrino factory is a very ambitious project
- Fortunately ASTeC and STFC is funding work on almost every area of it
- It might not be built in the UK
  - But there are several interesting opportunities for collaborations
    - Must not forget CERN and the US
- Talking of CERN, the LHC will decide what really gets built around 2011-12!