## Slide 1: Proximity Correction for Permanent Magnet + Iron Doublets
Stephen Brooks
2015-Mar-05

## Slide 2: Degrees of Freedom, Potentials
QF
BD
-U
U
V
-V
These are the pole potentials (white) for our doublet determined by midplane symmetry.
If U=V then QF should be a good quadrupole in its interior (design is based on potentials).
PM thicknesses (green) are from midplane symmetry and sum over magnetic circuit=0.
Three PM variables, three potentials to be set.
A
B
(A+B)/2
(A+B)/2
C
C/2
C/2
W
-W
0

## Slide 3: Method for Correction
Simulate baseline doublet with interference and wrong fields 
  Get Az component of the potential from simulation at each pole, giving values of U, V, W
    This can be either at centre of pole or average along pole in z
    Potential at midplane should probably be zero but if it isn’t, subtract it off
Simulate doublet with A, B, C values increased by say 1mm in turn, consistent with previous diagram
  Get Az component and U, V, W from each simulation
Use the 4 simulations and 12 potential values above to contruct a local linear model
  u(a+d) = u(a) + Md
  Where: u = (U, V, W), a = (A, B, C)
Use this to do a step of Newton’s method
  anew = a + M-1(udesired – u(a))
  udesired = (U, V, W) from simulations of the separate magnets
Repeat if necessary

## Slide 4: What Could Go Wrong
For very small separations, M might be:
  Singular, in which case no solution
  Ill-conditioned, in which case solution requires very large amounts of PM material
This may or may not work for 3cm separation
  Could try larger separations and “walk” it down
I think smaller separations will carry a penalty in requiring more material

## Slide 5: What Could Go Right
If enough PM material is included for 3cm operation, it can probably be partially short circuited to be correct for anything between that and separate magnet operation
This would use the short-circuit plate adjustment scheme Holger already envisioned for tuning the magnets
Should only require bench tuning
If we pull this off, it is innovative  publish
Could also work well for 2 full quads, in which case there are 4 variables and 4 potentials