## Slide 1: Muon1 “Dynamic Aperture” Scan
Using the first girder cell from CBETA note #1

## Slide 2: Setup
70 cells (just under a turn)
5000 particles
Particles killed at magnet apertures R~40mm
Vary fieldmap strengths from 0.88x to 1.08x
  Nominal is 0.98x on both
Colour points by transmission fraction

## Slide 3: Circular beam R=1cm
100% = p cm2
= 314 mm2
25% = 78.5 mm2
10% = 31.4 mm2
5% = 15.7 mm2
(0.98,0.98)
QF strength
BD strength
1.00
0.90
0.90
1.00

## Slide 4: Circular beam R=1cm
100% = p cm2
= 314 mm2
25% = 78.5 mm2
10% = 31.4 mm2
5% = 15.7 mm2
(0.98,0.98)
QF strength
BD strength
1.00
0.90
0.90
1.00
Qx=1/3
Qy=1/3
Qy=1/4 (?)

## Slide 5: Circular beam R=3cm
(0.98,0.98)
QF strength
BD strength
1.00
0.90
0.90
1.00
100% = 9p cm2
= 2827 mm2
5% = 141 mm2
2% = 56.5 mm2
1% = 28.3 mm2

## Slide 6: Results
I only see n/3 and n/4 (faintly) resonances
Francois and Scott have seen 2/5 and 3/8
Where’s the difference? Possibilities:
  Different test particle distribution/algorithm
  Francois is scanning in energy rather than field
  I’m staying in the same place rather than re-matching the closed orbit each time
  I don’t vary angles, just entrance positions

## Slide 7: Future
I can try doing what Francois is doing
  Scan in energy
  Find closed orbit at each energy
  Launch particles around it in Muon1
Francois can try and do what I’m doing
  Vary the strength of the 2 fieldmaps
  Test the transmission of ~70 cells in Zgoubi