## Slide 1: Muon1 Results for the FFAG Arc Cell using Fieldmaps
The “v4” magnets and FFAG cell update as described in CBETA note #9

## Slide 2: Fieldmaps Used
By Nick Tsoupas (Box: project, 1.05, fieldmaps)
  QF_v4_x=+-4p1y=+-1p4z=+-25_stp=1mm_nodal_Br=1p204_Hc=-1p19_N35EH
  BD_v4_x=+-4p1y=+-1p4z=+-25_stp=1mm_nodal_Br=1p204_Hc=-1p19_N35EH
Jim Crittenden did fieldmaps with the same parameters, giving nearly identical results in tracking (it doesn’t matter)

## Slide 3: Muon1 Results
Parameter | Muon1 soft-edge 2.5cm | Fieldmap nominal | Fieldmap 100% | Nominal w/ BD offset | 100% with BD offset
Fieldmap scaling factor | N/A | 98% | 100% | 98% | 100%
BD X offset | 0 | 0 | 0 | -0.45mm | -0.95mm
Qx (42MeV) | 0.3668 | 0.3630 | 0.3758 | 0.3615 | 0.3724
Qy (42MeV) | 0.2912 | 0.2834 | 0.2921 | 0.2821 | 0.2892
Qx+2Qy (42) | 0.9492 | 0.9298 | 0.9600 | 0.9257 | 0.9508
Qy (150) | 0.0362 | 0.0342 | 0.0356 | 0.0346 | 0.0363
QF Xmin | -22.70mm | -24.06mm | -23.97mm | -23.48mm | -22.78mm
QF Xmax | +22.75mm | +22.09mm | +19.85mm | +23.44mm | +22.69mm

## Slide 4: Integrated* Fields
Parameter | Muon1 soft-edge 2.5cm | Fieldmap nominal | Fieldmap 100% | Nominal w/ BD offset | 100% with BD offset
Fieldmap scaling factor | N/A | 98% | 100% | 98% | 100%
BD X offset | 0 | 0 | 0 | -0.45mm | -0.95mm
Qx (42MeV) | 0.3668 | 0.3630 | 0.3758 | 0.3615 | 0.3724
Qy (42MeV) | 0.2912 | 0.2834 | 0.2921 | 0.2821 | 0.2892
QF grad T/m | -11.2 exact | -11.0134 | -11.2381 | -11.0134 | -11.2381
BD grad T/m | -10.7 exact | 10.5254 | 10.7402 | 10.5254 | 10.7402
BD dipole T | -0.309 exact | -0.303768 | -0.309967 | -0.299031 | -0.299764
* Field Z integrals divided by magnet nominal length (13.33cm QF, 12.17cm BD)