## Slide 1: PM_Correct CBETA Magnet Software

## Slide 2: Introduction
Command-line utility that runs on Windows
Uses a config.txt file that specifies:
  Target parameters for all magnets
    Different types are identified by numerical id ranges
  Wire tuning parameters
  Systematic file input/output locations
Re-centers the harmonics and also outputs tuning wire lengths

## Slide 3: Config File

## Slide 4: Adjustment to Goal Parameters
I recently found magnet tuning targets were out of date in my software
  Scott Berg confirmed the baseline parameters were also out of date
  I had to re-do a pair of tuning wire cartridges
New fields targets about 1% stronger, based on 3D not 2D models (as it should be)
Most magnets should be fine, the BD1 is now slightly marginal as we’ll see

## Slide 5: Running on BD1 Run 4

## Slide 6: Initially Arbitrary Quality Feedback
CBETA multipoles FOM
  >0.75 Bad, 0.5-0.75 Marginal, 0.25-0.5 Fair, 0.1-0.25 Good, <0.1 Excellent
Quad strength error
  >0.2% Bad, 0.1-0.2% Fair, 0.05-0.1% Good, <0.05% Excellent
We can customise this

## Slide 7: Running on BD3 Run 12

## Slide 8: Program Outputs
CSV table of re-centered harmonics
  Includes displacement and rotation relative to coil
Tuned magnet design CSV file include wire lengths
Not yet implemented, can be if needed:
  Human-readable log/quality report
  (More) human-readable wire lengths table
  Subsequent iterations based on results from an already-tuned magnet

## Slide 9: Storage Update
Currently have access to two SMD shares:
  \\DISCOVERY\C_Beta
    Contains random LEREC files(?), probably needs to be pointed at a different folder
    I have write access on \\DISCOVERY\C_Beta\NOTES
  \\DISCOVERY\NewData
    Contains rotating coil .dat files in the format my software can read
    Not sure how long files stay on there so I should probably copy them into the CBETA share too