## Slide 1: CBETA Magnets 1301, 1302
First girder BD1, BD2

## Slide 2: Last Week
Mon: John C. on holiday
Tue, Wed: drilling baseplate fiducials and installing second Faro arm base further from the coil
Thu: p.m. first measure of BD1
Fri: BD1 survey, measure, rotate 180, measure, survey (ideal day)
Mon: a.m. wasted time on water fittings, p.m. BD2 measure, survey, tune, measure

## Slide 3: 1301 / FG BD1 History
Run # | Max error on midplane (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
1 | ? | +3.436% | 175.68 | 5.131 | Very large panel gap
4 | 43.50 | -0.334% | 105.15 | 3.441 | Rebuilt for alignment
19 | 8.05 | +0.060% | 23.79 | 0.780 | Wire tuning iteration 1
20 | 8.06 | +0.058% | 23.55 | 0.773 | Redone on Friday
21 | 8.40 | +0.046% | 23.43 | 0.770 | End-for-end rotated

## Slide 4: BD1 Tuned Harmonics
-11049.47 | 0.00
10000.00 | 0.00
-1.79 | 0.33
-21.61 | 3.95
-4.81 | -2.41
-1.42 | -2.08
-3.14 | -3.03
-1.07 | -2.25
0.94 | -0.70
-0.64 | -0.34
-0.90 | -0.94
-1.02 | -0.88
1.33 | 0.50
0.30 | 0.32
0.27 | 0.14
-0.20 | -0.14
-0.12 | -0.10
0.23 | 0.02
-0.03 | -0.01
-0.02 | 0.04

## Slide 5: BD1 Comments
First tuning iteration gave a 4x improvement but starting from a low base
Probably a good candidate for a 2nd tuning iteration because the code thinks it can do it

## Slide 6: 1302 / FG BD2 History
Run # | Max error on midplane (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
3 | ? | Wrong temperature | 12.00 | 0.387 | Wire tuning iteration 2 but wrong temperature
4 | 28.34 | -0.921% | 10.78 | 0.371 | Remeasured at 85F
5 | 21.63 | +0.973% | 108.94 | 3.329 | Wire tuning iteration – script error! Wrong wire assumption

## Slide 7: BD2 Comments
Here, there was a variable name error in the new PM_Correct tool, so the program assumed the magnet had no wires in it already, leading to an overcorrection
After error fixed, code produces a tuning and predicts 13.7 units error (not so good) but minus 0.017% strength error (OK)
  Might need another iteration once back in the right strength region to finish this off

## Slide 8: All FG Magnets Status
Magnet name | Max error on midplane (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
BD1 (rb) | 8.06 | +0.058% | 23.55 | 0.773 | New iter 1
BD2 | 28.34 | -0.921% | 10.78 | 0.371 | Run 4
BD3 (rb) | ? | Wrong goal | 68.83 | 2.204 | Old iter 0
BD4 | ? | Wrong temp | 9.13 | 0.247 | Old iter 2
QF1 | ? | Wrong temp | 3.38 | 0.114 | Old iter 1
QF2 | ? | Wrong goal | 7.30 | 0.149 | Old iter 1
QF3 (ra) | ? | Wrong goal | 4.78 | 0.099 | Old iter 2
QF4 (ra) | ? | Wrong temp | 21.25 | 0.273 | Old iter 1
(rb) = rebuilt, (ra) = reassembled from halves

## Slide 9: Next “Week” (3 days)
Tue: a.m. BD2 survey, p.m. new BD2 wire set
Wed: BD3 (already have 1st iter wire set)
  Meanwhile, add water fittings to BD4
Thu-Sun: Thanksgiving
Mon: BD4
  Needs an E4E roll angle check and then BD series first pass done
  Need to do HMAC-requested extra iterations