## Slide 1: CBETA Magnet 1504 and Survey
First girder QF4

## Slide 2: Last Week
Tue: one iteration on QF4, was OK, surveyed plus E4E survey
Wed: George unmount QF4
Thu: (Weds and today John C. out sick)
Fri: Earth’s magnetic field & amplifier test
  Sat: BDH assembled
Mon: BD1 iteration with 105mil wire
  Drilled pins into BDH

## Slide 3: 1504 / FG QF4 History
Run # | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
3 | ? | Wrong temperature | 21.25 | 0.273 | Iteration 1 but at wrong temp. and reassembled badly
4 | 11.33 | -0.170% | 28.49 | 1.123 | Bare magnet remeasured at 85F
5 | 1.35 | +0.068% | 6.48 | 0.200 | Wire iteration 1, surveyed
6 | 1.58 | +0.076% | 6.70 | 0.204 | E4E survey
* New definition with retuned position

## Slide 4: QF4 Comments
Did quite well in a single iteration
  Didn’t quite get to 1 Gauss error, but close
  One of our best bare magnets too
Finished off with an E4E to check coil roll angle

## Slide 5: Harmonics QF4
-1.53884 | 0
-1.31E-61 | -2.46E-61
10000 | 1.24E-12
-1.86477 | 2.610895
-3.18878 | -1.90281
3.02891 | -1.348
0.195031 | 0.410219
-1.09532 | 0.305111
1.196406 | -1.16666
0.757533 | 0.79611
-0.96574 | -0.02911
0.019095 | -0.43973
0.38387 | 0.175195
-0.16887 | 0.143262
-0.12216 | -0.17685
0.133611 | 0.004752
-0.02808 | 0.070035
-0.05599 | -0.08572
0.145224 | 0.058035
0.004062 | -0.00866
-0.04747 | 0.006167
Displaced magnet by DX (m) | -0.00041
DY (m) | -0.00142
Rotated A/C by (rad) | 0.008458
(deg) | 0.484594

## Slide 6: 1301 / FG BD1 History
Run # | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
1 | ? | +3.436% | 175.68 | 5.131 | Very large panel gap
4 | 26.64 | -0.334% | 105.15 | 3.441 | Rebuilt for alignment
19 | 4.07 | +0.060% | 23.79 | 0.780 | Wire tuning iteration 1 (80mil)
20 | 4.07 | +0.058% | 23.55 | 0.773 | Redone on Friday
21 | 4.23 | +0.046% | 23.43 | 0.770 | End-for-end rotated
22 | 3.64 | -0.267% | 20.54 | 0.670 | 105mil iteration based on run 20, possible error
* New definition with retuned position

## Slide 7: All FG Magnets Status
Magnet name | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes | Run #
BD1 (rb) | 4.07 | +0.058% | 23.55 | 0.773 | New iter 1 | 20
BD2 | 2.63 | -0.196% | 19.28 | 0.539 | 105mil wire | 8
BD3 (rb) | 0.98 | +0.030% | 9.05 | 0.265 | New iter 2 | 15
BD4 | 1.03 | +0.045% | 11.62 | 0.167 | New iter 3 | 9
QF1 | 1.82 | -0.036% | 6.18 | 0.118 | New iter 2 | 6
QF2 | 1.06 | -0.047% | 7.22 | 0.110 | New iter 1 | 34
QF3 (ra) | 0.94 | -0.006% | 10.26 | 0.226 | New iter 2 | 20
QF4 (ra) | 1.35 | +0.068% | 6.48 | 0.200 | New iter 1 | 5
* New definition with retuned position
(rb) = rebuilt, (ra) = reassembled from halves

## Slide 8: Earth’s Field
Nominal length is 1m so harmonic values that follow are just in Tesla, Tesla/m etc.

## Slide 9: Earth’s Field
-5.84E-05 | 0
10000 | -1.37E-12
-236.242 | 79.30331
10.62145 | 22.1937
-1.74972 | 5.823054
-1.58629 | 0.106668
5.185104 | 3.909303
0.684718 | 0.384219
-0.52332 | -1.20218
-0.38583 | 0.588972
0.196431 | -1.66913
-0.68447 | -0.42182
0.443626 | -1.16287
0.817974 | -1.71284
0.569647 | 0.820994
1.055952 | -0.33229
-0.29859 | 1.958616
-1.15328 | -1.70581
0.111302 | -2.13486
2.093805 | -0.82845
-0.82551 | -0.78096
Displaced magnet by DX (m) | 0
DY (m) | 0
Rotated A/C by (rad) | -0.44327
(deg) | -25.3977
0.584 Gauss field pointing at 25.4 degrees from vertically downward
Coil gets 0.584 Gauss.m
Our integrated gradients are ~1.35 T for BD for example (NB: short magnets!)
Corresponds to displacement of 0.584e-4/1.35 = 43 microns
Of course we don’t know what the Earth’s field is in the L0E hall but at least we can subtract it here.

## Slide 10: BDH almost done
Thanks to George for putting this together on Saturday
Pinned on Monday

## Slide 11: Raw Survey Data Files
Have these for all magnets now, double for the four E4E runs (QF1,4, BD1,4)
Fairly minimal: just the magnet and baseplate fiducials, the coil axis and magnet endplanes.

## Slide 12: PM_CoilRoll
 Currently filling in this data structure

## Slide 13: Next Week
Tue: BDH measurement
Wed: BDH tuning
Thu, Fri, Mon: Back to finishing BD1, BD2
  And then we’ll be done for magnet fields
  I’ll continue to develop survey software