## Slide 1: CBETA Magnet 2401
First production articles QD

## Slide 2: Tuning of Magnet
Magnet # | Run # | Midplane error (G) | Units FOM | CBETA FOM | Quad error at x=0 (rel.)
2401 | 1 (bare) | 23.18 | 37.41 | 1.512 | -0.693%
 | 2 (iter 1) | 0.80 | 2.40 | 0.096 | -0.016%
Goals |  | ≤ 1.5 | ≤ 10 | ≤ 0.375 | ≤ 0.05% (Q)

## Slide 3: Harmonics of Tuned Magnet
Magnet 2401
1.359278 | 0
-6.29E-66 | 1.29E-65
10000 | 4.74E-14
0.30134 | -0.19836
0.094461 | 0.628895
-0.25839 | -0.89401
-1.90665 | 0.537498
-0.0626 | 0.380555
0.370024 | -0.01775
0.199319 | -0.25305
0.088492 | -0.10172
0.048435 | -0.08821
0.082022 | -0.08426
-0.04311 | 0.016163
-0.04353 | 0.008469
-0.0115 | -0.00303
0.007529 | -0.01013
-0.01331 | 0.010135
0.07983 | 0.000845
-0.00865 | -0.0098
-0.00273 | 0.003698
Displaced magnet by DX (m) | -0.00036
DY (m) | -0.00086
Rotated A/C by (rad) | 0.032804
(deg) | 1.879537

## Slide 4: Status
QD magnet 2401 is tuned + surveyed
QD magnet 2402 has been measured untuned
  Will be used as calibration between coil benches, while not tuned, to see harmonics
Might try getting Toby Levine to assemble shim pack for 2402
QDs both shows -0.7% strength offset so will probably change radius for next 3