## Slide 1: Test of Linear-Field Fixed-Field Arc with a Wide Energy Range
Tested at the BNL ATF-1 facility

## Slide 2: Outline of Main Components
ATF beam pipe
1” diam.
2” diam.
Flexible bellows and flange size adapter
FFA pipe through magnets
Fixed table
Movable table
Beam screen (FFA) and camera
Beam stop
Injection X position and angle adjustment
Beam direction
Screen (POP11)
Screen (POP10)
Triplet
Steerer (GT7)
Steerer (GT3)
For each energy, do 2D steerer current scans
  GT3X, GT7X (x,x’)
  GT3Y, GT7Y (y,y’)
  GT7X, GT7Y (x,y)
Plus four larger-range 1D scans and a quad scan of the triplet

## Slide 3: Tracking of (x,x’) Offsets
Trajectories have been magnified transversely by 16x for visibility
xin ±1mm
x’in ±10mrad

## Slide 4: ATF-FFA Beamline Parameters
Parameter | Value | Units
Particle species | Electron | 
Energy range | 18-72 | MeV
Cell Length | 0.234301 | m
Cell Angle | 6.666… | degrees (54 per turn)
R = avg. radius of curvature | 2.01367 | m
Max orbit excursion | 18.21 | mm (from circle radius R)
Tune range per cell | Qy,72 = 0.029, Qx,18 = 0.411 | cycles
Cell lattice | halfD2, QF, D1, BD, halfD2 | 
Drift lengths | D1 = 57.35, D2 = 57.65 | mm
Number of cells | 6 | 
Total length | 1.40581 | m
Total angle | 40 | degrees

## Slide 5: EMMA Comparison (pros and cons)
Parameter | EMMA | ATF-FFA | Units
Energy range | 10.0–20.0 | 18.0–70.489 | MeV kinetic energy
Momentum ratio | 1.952 | 3.837 | ×
Radius of curvature | 2.63720 | 2.01367 | m
Effective avg. dipole | 0.02593 | 0.11761 | T
Total angle | 360 | 40 | degrees
Operation mode | Storage ring | Transfer line | 
Acceleration? | Yes (lots!) | None | 
Lattice | Doublet | Very close to FODO | 
Cell length | 0.394524 | 0.234301 | m
Cells per turn | 42 | 54 (extrapolated) | 
Length built | 16.57 | 1.40581 | m

## Slide 6: Matched Orbits through Fieldmaps
18, 24, 36, 54, 72MeV

## Slide 7: Beams Exit from Periodic Cell

## Slide 8: Magnet Design and Parameters
Parameter | “QF” magnet | “BD” magnet | Units
Length | 57.44 | 61.86 | mm
Dipole By(x=0) | 0 | -0.37679 | T
Quadrupole dBy/dx | -23.624 | 19.119 | T/m
Inner radius (magnet pieces) | 37.20 | 30.70 | mm
(shim holder) | 34.70 | 27.60 | mm
“Pole-tip” field (magnet pieces) | 0.879 | (-)0.964 | T
Outer radius (magnet pieces) | 62.45 | 59.43 | mm
(tubular support) | 76.2 | 76.2 | mm
QF
BD
S.J. Brooks, “Production of Low Cost, High Field Quality Halbach Magnets”, Proc. IPAC’17

## Slide 9
All the magnets had already been built as part of CBETA R&D and all have had iron wires inserted.

## Slide 10: Radii/Clearances
 | Radius wrt torus (mm) | Distance to previous (mm)
Maximum beam excursion | 18.21 | 
Vacuum pipe inside | 23.75 | 5.54 (12.00 in CBETA)
Vacuum pipe outside | 25.40 | 1.65 (pipe thickness)
Shim holder inside (BD) | 27.45 (27.60 straight) | 2.05 (air gap)
PM block inside edges (BD) | 30.55 (30.70 straight) | 3.10 (shim holder)
May have been a bit over-optimistic with beam clearance, seeing scraping near 36MeV
Re-aligned pipe after 36MeV run because it was being pulled off-centre by bellows

## Slide 11: Girder and Supports Construction
Feb 22, 2017

## Slide 12: Detail: Magnets on the Girder
Apr 7, 2017

## Slide 13: Pipe undergoing Leak Check
Apr 14, 2017

## Slide 14: Picture of Everyone Standing By It
ATF experiment AE79
May 1, 2017

## Slide 15: First Beam during Fault Studies
May 4, 2017
54MeV was the first energy to be tested

## Slide 16: With Survey “Faro Arm” Attached
May 5, 2017
Most magnet offsets <0.2mm; RMS 0.1mm or better

## Slide 17: Beam X,Y Scan at 54MeV
May 8-9, 2017
Tracking model:
Qx = 0.119
Qy = 0.055
6Qx = 0.713
6Qy = 0.329
Each setting in the 2D current scan is given a colour and all the 11*11 beams at each diagnostic overlayed
POP10
POP11
FFA

## Slide 18: Beam X,Y Scan at 36MeV
May 11-12, 2017
Tracking model:
Qx = 0.176
Qy = 0.122
6Qx = 1.056
6Qy = 0.734
Here we encountered beam scraping quite close (~2mm away) to the nominal closed orbit
Later turned out to be injection and pipe misalignment, fixed on later runs
POP10
POP11
FFA

## Slide 19: Interlude: IPAC’17
May 18, 2017

## Slide 20: Beam X,Y Scan at 70MeV
Jun 20, 2017
Tracking model:
Qx = 0.098
Qy = 0.029
6Qx = 0.587
6Qy = 0.175
The FFA was aligned for 72MeV k.e. but ATF could only do 70.489MeV
Accepted results taking energy error into account in tracking (hence rightward shift)
POP10
POP11
FFA

## Slide 21: Beam X,Y Scan at 24MeV
Jun 23, 2017
Tracking model:
Qx = 0.271
Qy = 0.212
6Qx = 1.629
6Qy = 1.274
At 24MeV and below, the ATF beam becomes much larger due to deceleration in second linac section
Horizontal scraping on the vacuum pipe is visible on both sides
POP10
POP11
FFA

## Slide 22: Aligned at 18MeV: Extreme Angle
Jun 28, 2017

## Slide 23: Aligned at 18MeV: Kinked Bellows
Jun 28, 2017

## Slide 24: Beam X,Y Scan at 18MeV
Jul 3, 2017
Tracking model:
Qx = 0.411
Qy = 0.312
6Qx = 2.463
6Qy = 1.871
Beam got through once again showing X scraping on both sides, but with different vertical phase advance
Experiment complete!
Uninstalled by end of July
POP10
POP11
FFA

## Slide 25: (Almost) all the Data
Quad scan is not on this plot
Torrent of the results is available at http://stephenbrooks.org/ap/ATF-FFA
(5 energies)*(8 scans)*(31–121 points)*(3 screens)*(3–5 pulses) = 25113 images

## Slide 26: All Energies Phase Advance

## Slide 28: 54MeV Results vs. Raw Tracking

## Slide 29: Input Camera Roll Angle Correction
Looks better, has some offset.

## Slide 30: Fitting X,Y Offset at Output
Required shift:
(1.84,0.38)mm

## Slide 31: Transfer Matrix XX Element
“Measurement” is just taking the difference of a pair of centroids in the good area of the scan

## Slide 32: Transfer Matrix YY Element

## Slide 33: Source Code, Open Data
Torrent of the results is available at http://stephenbrooks.org/ap/ATF-FFA

## Slide 34: Conclusion & Future Plans
Beam has turned a nontrivial angle (40°) in six cells of a non-scaling FFA
  Over a 3.8x momentum range (NS-FFA record)
  At an energy of up to 70MeV (NS-FFA record)
  Using compact permanent magnet technology
No highly nonlinear aberrations seen
  More data processing needed to get good fit to tracking at lower energies
Demonstrates technology for CBETA and more

## Slide 35: CBETA Magnet Production
and non-scaling FFA proliferation

## Slide 36: What is CBETA?
It’s a non-scaling (linear field) FFA
It’s an energy-recovery linac (ERL)
It’s both at the same time
  EMMA was an FFA ring with ERL injector (ALICE)
  CBETA is a racetrack FFA with linac inside it
Dejan has probably explained this already

## Slide 37: EMMA/ATF/CBETA Comparison
Parameter | EMMA | ATF-FFA | CBETA girder | CBETA (future) | Units
Energy range | 10.0–20.0 | 18.0–70.5 | 37.5–58.5 | 41.5–149.5 | MeV k.e.
Momentum ratio | 1.953 | 3.837 | 1.553 | 3.572 | ×
Radius of curvature | 2.63720 | 2.01367 | 5.08787 | 5.08787–∞ | m
Effective avg. dipole | 0.02594 | 0.11761 | (0.09834) | 0.09834 | T
Total angle | 360 | 40 | 20 | 280 | degrees
Operation mode | Storage ring | Transfer line | Transfer line | ERL | 
Acceleration? | Yes (lots!) | None | None | Yes (linac) | 
Lattice | Doublet | Close to FODO | Doublet | Doublet | 
Cell length | 0.394524 | 0.234301 | 0.444 | 0.444 | m
Cells per turn | 42 | 54 (extrapolated) | 72 (extrapolated) | 107.5 (racetrack) | 
Length built | 16.57 | 1.40581 | 1.776 | 47.73 | m

## Slide 38: Timeline
Summer 2017: ATF-FFA girder with beam at BNL, 3.8x momentum range (my FFA’17 talk)
  12 permanent magnets
May 2018: CBETA girder beam test at Cornell
Nov 2018: CBETA magnet+girder production complete
  216 permanent magnets
March 2019: CBETA commissioning starts

## Slide 39
CBETA first splitter line and first FFA girder at Cornell (May 2018)
FFA girder

## Slide 40: Cell Tunes × 3
NB: ATF-FFA’s data fit is on matrix elements not tunes (graphs on bottom row)
EMMA
ATF-FFA
CBETA girder test
data
model

## Slide 41: Girder Production Complete (Nov 2018 at BNL)

## Slide 42: CBETA as of Jan 1, 2019 (at Cornell)

## Slide 43
CBETA first FFA girder at BNL
Half-length magnet for matching

## Slide 44
CBETA first FFA girder under construction at BNL

## Slide 45
CBETA permanent magnet containing tuning wire insert

## Slide 46: Magnet Types and Parameters
QF
BD
QD
BDT2
BDT1
Magnet | Dipole (T) | Quad (T/m) | Good field radius (mm) | Aperture radius (mm) | Max field (T) (good region) | Max field (T) (aperture)
QF | 0 | -11.5624 | 25 | 43.1 | 0.2891 | 0.4983
BD | -0.3081 | 11.1475 | 25 | 40.1 | 0.5868 | 0.7551
BDT2 | -0.2543 | 11.1475 | 25 | 44.938 | 0.5330 | 0.7552
BDT1 | -0.1002 | 11.1475 | 25 | 49.085 | 0.3789 | 0.6474
QD | 0 | 11.1434 | 25 | 40.1 | 0.2786 | 0.4469

## Slide 47: Layout and Magnet Counts
Permanent magnet total: 216
QF: 107
BD: 32
BDT2: 20
BDT1: 28
QD: 27
QFH: 1 (half length)
BDH: 1

## Slide 48: Production and Testing Flow
AllStar
PM wedges
KYMA
assembly
1
3
2
4
BNL
tuning
5
Accept
Helmholtz testing at AllStar, 100% of blocks but not temperature controlled
Temperature-controlled Helmholtz test of ~15% sample at BNL for verification
Remainder of blocks shipped directly to KYMA, who also re-test ~10% sample
Rotating coil measurement of bare magnet at BNL
Rotating coil measurement of tuned magnet at BNL

## Slide 49
100% complete (excl. spares*)
215 / 215 magnets (0 remaining)
* We have 4 “spare” QFs, 2 BDs for replacing first girder magnets, plus two spare BDT2 magnets, with more spares to be delivered from KYMA

## Slide 50
BDT1 28 / 28 magnets (0 remaining)
BDT2 22 / 20 magnets (2 spare)
BD 30 / 32 magnets (2 remaining*)
QD 27 / 27 magnets (0 remaining)
QF 107 / 107 magnets (0 remaining)
QFH 1 / 1 magnet (0 remaining)
* Total of 32 includes 4 spares for replacing the first girder BDs (same applies to QF total)

## Slide 51: Final Measurement Rate
Main Production | 
Magnets tuned | 200 (excl. early samples)
Rotating coil measurements | 545
Start date | July 9, 2018
End date | November 14, 2018
Total weeks | 18.2
Magnets tuned per week (avg.) | 10.96
Rotating coil meas. per week (avg.) | 29.88
Rotating coil meas. per magnet (avg.) | 2.73

## Slide 52
Permanent magnets shipped from KYMA

## Slide 53
Rotating coil magnet measurement at BNL

## Slide 54
Rotating coil magnet measurement at BNL

## Slide 55
Wire tuning packs for CBETA magnets

## Slide 56: Tuned Magnets Criteria
Midplane error (G) | Units FOM | CBETA FOM | Quad error at x=0 (rel.)
≤ 1.5 | ≤ 10 | ≤ 0.375 | ≤ 0.05% (Q)
Unit = 10-4 of main pole
FOM is sqrt(sum of all (multipoles in units)2)
  CBETA FOM is weighted version based on tracking
Midplane error generally hardest to achieve
  May go in and out of spec slightly (~0.5G) due to chiller cycle

## Slide 57: Example Harmonics (QF 2566)
-1.53782 | 0
8.20E-64 | 1.87E-65
10000 | 1.26E-12
-0.2922 | -0.58294
-0.07957 | 0.201785
0.572878 | -0.88759
-0.44538 | -0.60878
0.015517 | -0.12825
0.064316 | -0.07939
0.038948 | 0.018125
0.051198 | 0.022414
0.037202 | -0.01268
-0.01854 | -0.01006
-0.01217 | -0.07378
-0.09591 | -0.03929
-0.00478 | 0.020399
-0.01032 | -0.01952
0.007539 | 0.007748
0.068582 | 0.001058
-0.00071 | 0.001648
-0.00187 | -0.00071
Displaced magnet by DX (m) | -0.0002
DY (m) | -0.00156
Rotated A/C by (rad) | 0.041074
(deg) | 2.353343
Reference radius (m) | 0.025
Normal
Skew
Integrated strength (T/m.m)
Dipole
Quad
Sext
Oct
etc.

## Slide 58
Only tuned magnets shown (2 “rejects” removed)
Tuned with 96 shims
80 shims
Reject matched with good half
Reject matched with good half
BD
QF
QD
BDT2
QFH
BDT1

## Slide 59
Only tuned magnets shown (2 “rejects” removed)
BD
QF
QD
BDT2
QFH
BDT1

## Slide 60
Only tuned magnets shown (2 “rejects” removed)
BD
QF
QD
BDT2
QFH
BDT1

## Slide 61: Water Cooling Stability

## Slide 62: Rejects/Repaired
BD 2305
Harmonics simulation w/swap
QF 2509
Harmonics simulation w/swap
QD 2427
Harmonics sim. w/type change
QF 2572
Harmonics sim. w/type change

## Slide 63: Reversed Block in QF 2509

## Slide 64
CBETA windowframe correctors at BNL

## Slide 65
CBETA girder production at BNL

## Slide 66: Other Problems/Lessons Learned
@BNL
  Warehouse roof leaks, hence tent in photo
  Gaps when reassembling magnets from halves
@AllStar
  Some blocks went rusty (not passivated?), had them re-made
  One type magnetisation angle was out-of-spec, had them re-made
@KYMA
  Couple of blocks inserted backwards
  One glue failure, exploding magnet, repaired
Team effort
  Block width with chamfer was not communicated clearly to AllStar, meaning blocks slightly larger than needed, had trouble fitting
  Chinese sign convention for magnetisation was opposite, had to invert blocks

## Slide 67: Backup (CBETA magnets)

## Slide 68: Helmholtz Measurements
Example: AllStar data for wedge types P1 through P16 (BD magnet)
Angle errors Strength variation

## Slide 69: Magnetisation Angle Distributions
Requested that factory re-make types P15 and P16 to reduce systematic error.
These are the smallest blocks, so not critical, but re-make will improve quality of untuned magnets.
General request was for 1 degree RMS error, but can cope with some above and some below as we have here (see next slide)

## Slide 70: Magnet Error Model
Both the strength and angle error distribution can be put back into the field simulation
Example: BD magnet using AllStar’s data set.
1000 magnets were generated, some with position errors. Histogram is binned by the “units FOM”.
Green = easy to tune
Red = possible problems
Based on first girder experience.

## Slide 71: BACKUP (ATF)

## Slide 72: Evidence of Camera Roll Angle
These scan patterns formed by energising the same corrector
Could also be mirror angle errors (multiple mirrors also involved)
y
x
POP10 estimated 2.6° clockwise
POP11 estimated 3° anticlockwise
y
x

## Slide 73: 36MeV Results vs. Raw Tracking

## Slide 74: Input Camera Roll Angle Correction
“Perspective” nonlinearity reproduced.
Looks like offset
could be at start
of beamline not
end.
NB: input positions measured relative to HeNe laser, which has thermal drifts, not necessarily actual axis of ATF beamline…

## Slide 75: Fitting X,Y Offset at Output
Required shift:
(-3.96,0.21)mm

## Slide 77: 70MeV Results vs. Tracking

## Slide 78: Fitting X,Y Offset at Output
Required shift:
(3.15,-0.09)mm

## Slide 79: 24MeV Results vs. Tracking
Seems to be at an X focus.
Tracking has different sign of X movement, but near zero in either case.

## Slide 80: 18MeV Results vs. “Tracking”
Tracking went wrong with measured centroids (particles falling out of fieldmap?)
Probably need to apply input shift in order to make the tracked particles go through (white dot is periodic orbit).

## Slide 81: 18MeV with Input Shift (arbitrary)
Picked a beam that got through and applied an input shift to put it on the closed orbit.
Required shift:
(-2.60,-2.65)mm

## Slide 82: 18MeV with Input Shift (no FM)
Replaced OPERA-3D fieldmaps by Muon1 soft-edge field model.
Much better!
Should check not going out of bounds in fieldmaps or something.

## Slide 83: Input/Output Position at 54MeV

## Slide 84: Input/Output Position at 36MeV

## Slide 85: 24MeV Results vs. Tracking (no FM)
Replaced OPERA-3D fieldmaps by Muon1 soft-edge field model.
X movement has right sign.

## Slide 86: Compensating for Output Offset

## Slide 87: Errors vs. Tracking, Output Offset

## Slide 88: Best Fit X,Y Offsets at Output

## Slide 89: Best Fit X,Y Offsets at Output