## Slide 1: CEBAF 20GeV FFA Upgrade
First attempts at permanent magnets
Comparison of 1 vs. 2 FFA loops
More-optimised magnet designs

## Slide 2: CEBAF ~20GeV FFA Upgrade
CEBAF is currently a 5.5-turn racetrack RLA
  123MeV injector, 1090MeV North & South linacs
  Maximum output energy 12GeV
  Five stacked electromagnetic arcs on East & West
Propose replacing one or two EM lines by multi-pass FFAs for extended energy reach
  R=80.6m so 20GeV  0.83T mean bending field
  Non-scaling FFAs used for magnetic efficiency
  Permanent magnets uses for power, cost savings
More in Ryan Bodenstein’s talk

## Slide 3: Parameters from IPAC’21 Paper
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 250.91 | -5 | 4 | -0.574 | 1.685
BD | 0.941 | -233.13 | -5 | 4 | 2.107 | 0.008
Take parameters directly from the paper
Note peak fields
20-24 GeV FFA CEBAF Energy Upgrade, S.A. Bogacz et al., Proc. IPAC’21

## Slide 4: Permanent Magnet Design Rules
Open midplane full height of 4mm (y=±2mm)
  Same as NSLS-IIU upgrade magnet (2020)
    Which is also 250T/m
Beam-centroid-to-magnet clearance of 5mm
  Again, same as NSLSII-U, has R=5mm aperture
Br=1.30T material
  E.g. AllStar N42EH grade
    Intrinsic coercivity Hcj=29.0kOe (without radiation)
      I.e. demagnetises totally at m0H=-2.9T (expect “knee” ~-2.7T)

## Slide 5: Run HalbachArea Script
https://stephenbrooks.org/ap/halbacharea/
Good field region of 9mm full width means:
  +/-4.5mm if re-centered in magnet
  Try Raperture=10mm to give >5mm clearance
Does not converge, fields 25% wrong

## Slide 6: Reduce to Raperture=7.5mm
Magnets converge but come out giant
BF
BD
>30cm
20.2 units error
14.4 units error
Also only 3mm from beam to magnet, probably not feasible

## Slide 7: Field Overshoot at High Gradient
The 5mm clearance distance translates to a larger field increase for higher gradients
  E.g. at 250.9T/m it corresponds to 1.255T
    Makes 2.107T max field into 3.272T at “pole tip”
  At 125.5T/m it corresponds to 0.627T
    Now only becomes 2.689T at pole tip
Not exact but gives idea of magnet difficulty
  Lower gradient can make magnet smaller even though good field aperture becomes larger

## Slide 8: FFA scaling* laws
Scaling type (by factor a) | Length | Angle | Dipole | Gradient | Quad offset (=dipole/grad) & orbit excursion
Momentum (~energy) | 1 | 1 | a | a | 1
Machine radius | a | 1 | a-1 | a-2 | a
FFA beta length (fixed bend radius, fixed cell tune) | a | a | 1 | a-2 | a2
FFA arc-to-straight (=row 3/row 2) | 1 | a | a | 1 | a
FFA radius with fixed orbit excursion and field (row 2*row 1/sqrt(row 3)) | a1/2 | a-1/2 | 1 | 1 | 1
* not scaling FFA laws
This one is the knob for changing gradients and orbit range: an engineering trade-off

## Slide 9: Lattice Scaled to 50% Gradient
Original
50% gradient, 2x beam excursion
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 250.91 | -5 | 4 | -0.574 | 1.685
BD | 0.941 | -233.13 | -5 | 4 | 2.107 | 0.008
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 125.46 | -10 | 8 | -0.574 | 1.685
BD | 0.941 | -116.57 | -10 | 8 | 2.107 | 0.008
NB: length and bend angles of elements to be multiplied by sqrt(2)

## Slide 10: Gradient Tradeoff Example
QF
BD
The gradient of the cell can be scaled, which results in orbits that are closer together but have the same magnetic field at each orbit. In other words, the dipole is constant but the gradient scales inversely with orbit separation.
The clearance requirements create an area optimum.
±10mm
58T/m
±14mm
41T/m
±18mm
32T/m
±25mm
23T/m
±35mm
17T/m
±50mm
12T/m
(All using CBETA clearances)

## Slide 11: Clearance Tradeoff Example
QF
BD
CBETA clearances
~12+2+3mm
Beam-centroid-to-pipe, pipe, pipe-to-magnet
Smaller clearances allow even more efficient magnets by increasing the gradient to the new higher optimum.
However, smaller clearances are harder to engineer and magnify relative errors from position misalignments.
Reduced clearances
6+2+3mm
and re-optimise gradient

## Slide 12: Clearance vs. Gradient Example

## Slide 13: Using Raperture=15mm (Rfield=10mm)
50% gradient scaled magnet converges with the full 5mm clearance
  But the magnets still come out giant!
BF
BD
4.8 units error
1.6 units error
>30cm

## Slide 14: Need Some Ideas (idea #1)
Now that Raperture=15mm…
There’s a lot of unused space above and below the beams
Could use “oval aperture” idea from Dejan’s hadron therapy gantry
  While still having an open midplane

## Slide 15: [IPAC’21] Halbach Magnet Variations
Demonstrated (in accelerator)
  Field tuning with iron rods
  Combined-function magnets
In development
  Open midplane magnets
Future research
  Oval apertures
  Multiple apertures

## Slide 16: Unused Region in BD (idea #2)
From the orbit diagram it appears that while
the orbits in BF are -5mm < x < 4mm,
the orbits in BD are -3.5mm < x < 3.25mm.
Don’t build magnet where you don’t need it!
BF
BD
BD

## Slide 17: Trimming the BD Aperture Range
50% gradient, 2x beam excursion
With reduced BD aperture range
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 125.46 | -10 | 8 | -0.574 | 1.685
BD | 0.941 | -116.57 | -10 | 8 | 2.107 | 0.008
NB: length and bend angles of elements to be multiplied by sqrt(2)
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 125.46 | -10 | 8 | -0.574 | 1.685
BD | 0.941 | -116.57 | -7 | 6.5 | 1.757 | 0.183
Peak fields better balanced between magnets (also minimises SR)

## Slide 18: Finally!
BF
BD
27.8 units error
24.1 units error
10cm
Small magnets, good field, full 5mm clearance
36.7cm2
40.5cm2

## Slide 19: Demagnetisation?
BF
BD
Red areas show m0H < -1.5T,
yellow -1.5 < m0H < -1.0T, etc.
Stripes are 0.1T intervals.
Looks like worst reverse flux value is around -2.3T, knee is -2.7T, likely OK without radiation but not much margin.

## Slide 20: B-H Curve and Demagnetisation
CBETA material grade N35H
External applied field (m0H)
opposing magnetisation direction
Net field (B)
Magnetisation provided by material (m0M = B − m0H)
Large opposing fields (negative H in the direction of M) can potentially demagnetise parts of the material in higher field magnets. Not observed or expected in CBETA (-H<1.3T). Depends on material grade Hcj value.
Hcj value (demagnetisation point,
varies with temperature)
Note: not N42EH, just example

## Slide 21: What about with 100% gradients?
BF converges but is still rather large
Probably should avoid super-high (>150T/m) gradients unless good reason
  E.g. path length
20cm

## Slide 22: Summary (IPAC’21 magnets)
Got a feasible magnet but had to employ several tricks:
  Scaled lattice to 50% gradient (double orbit range)
  Reduce circular aperture to vertically ±5mm oval
  Trim BD good field range to cover only orbits
Future work:
  Is 50% (~120T/m) gradient the optimum?
  Prediction of radiation dose limit (CBETA model)
Are any design rules/assumptions wrong?

## Slide 23: Existing 12GeV CEBAF Energies

## Slide 24: Upgraded CEBAF Injector Energy
Avoid large energy ratios in linacs to >20GeV
Three new RF modules of 90MeV each
  Two passes through these with a single conventional return loop
Use existing injector at 110MeV
Total energy: 110+2*(3*90) = 650MeV
110
90
90
90

## Slide 25: Energies with One FFA (4+7 turns)
Linacs adjusted 925-1090MeV for 50-100% energy tunability

## Slide 26: Energies with Two FFAs (3+(4+4))

## Slide 27: Energies with Two FFAs (3+(5+3))

## Slide 28: Lattice Optimisation Rules
Minimise maximum field on any beam orbit
Cell angle = 2° clockwise (-2°)
Overall radius of curvature = 80.6m
  Ensures cell length of 2.81347m
Both drifts are 10cm long
  Packing factor 92.9%
All cell tunes between 0.025-0.425, x,y planes
  Wide range to compensate for energy adjustment

## Slide 29: MAD-style Lattices
Parameter | One FFA | 4+4 FFA1 | 4+4 FFA2 | 5+3 FFA1 | 5+3 FFA2 | Units
Emin | 8.9 | 7.1 | 14 | 7.1 | 16 | GeV
Emax | 23 | 16 | 23 | 18 | 23 | GeV
Eref | 15.95 | 11.55 | 18.5 | 12.55 | 19.5 | GeV
BF length | 1.36109 | 2.09794 | 1.68482 | 1.57127 | 1.49155 | m
BF angle | -0.05722 | -1.73802 | -1.14623 | -0.65227 | -0.98835 | degrees
BF quad | -48.649 | -29.730 | -65.616 | -35.135 | -80.781 | T/m
BD length | 1.25238 | 0.51553 | 0.92865 | 1.04220 | 1.12192 | m
BD angle | -1.94278 | -0.26198 | -0.85377 | -1.34773 | -1.01165 | degrees
BD quad | 43.393 | 93.393 | 86.787 | 42.943 | 76.276 | T/m
Dipoles calculated from length, angle and Eref

## Slide 30: Max Field on Beams

## Slide 31: SR Loss Per Half-Turn

## Slide 32: Performance Comparison
Option | Max Field (T) | SR Loss (MeV) | Final Energy (MeV)
One FFA | 2.007 | 1211.48 | 23418.52
Two FFAs (4+4) | 1.495 | 964.44 | 23665.56
Two FFAs (5+3) | 1.489 | 935.30 | 23694.70
Two FFAs should be considerably better from magnet point of view, particularly radiation hardness due to the decreased fields

## Slide 33: Path Length

## Slide 34: Orbit Excursion
Lattice | Orbit range in BF (mm) | Orbit range in BD (mm)
One FFA | 56.74 | 41.57
4+4 FFA1 | 42.61 | 27.89
4+4 FFA2 | 21.34 | 14.05
5+3 FFA1 | 54.79 | 39.07
5+3 FFA2 | 14.95 | 10.66
Values given are full ranges (xmax-xmin)
  CBETA would be 50mm in focussing magnet
Generally the low energy FFA has a CBETA-like orbit excursion and FFA2 is much smaller
  Could go below 2°/cell in FFA1 to reduce range

## Slide 35: Summary (one vs. two FFAs)
Using two FFAs reduced maximum field on beam from ~2.0T to 1.5T
  Should lead to a substantial improvement in permanent magnet practicality
Two FFA design has 22% less synchrotron radiation power loss than one FFA
New lattices are baseline as of July 30th 2021
  “5+3” is marginally better than “4+4”

## Slide 36: Max Field on Beams
Magnet benchmark on 4+4 FFA2
because highest field in high-energy FFA

## Slide 37: Magnets for July 30th 4+4 FFA2
Wanted to replace central rectangular pieces with wedges to avoid slipping
  Reduce 32 to 24 pieces per magnet (CBETA=16)
BF
BD
27.1 units error
25.8 units error
27.8cm2
27.4cm2
5cm
~25% less area than IPAC’21 magnets
CBETA magnets were from 38cm2 to 78cm2
-65.6T/m
86.8 T/m

## Slide 38: Try Larger Clearances
NSLS-IIU recently doubled their exit slot height from 4mm to 8mm (y=±4mm)
  Allows vacuum chamber inside magnet
Could try doing the same
  Also double beam-to-magnet clearance from 5mm to 10mm (for 20mm full height central aperture)
Rescale gradients on July 30th lattice to 50% to avoid field overshoot in larger clearance gap

## Slide 39: ESRF Upgrade Chamber ~9mm Slot
Layout of the Vacuum System for a New ESRF Storage Ring, M. Hahn et al., Proc. IPAC’14

## Slide 40: Magnets: 4+4 FFA2, 50% gradient
September 10, 2021
BD
27.1 units error
105.8cm2
BF
32.5 units error
100.4cm2
Should be very similar, but 2x the size and 4x the area
10cm
CBETA magnets were from 38cm2 to 78cm2
-32.8T/m
43.4 T/m

## Slide 41: Demagnetisation in IPAC’21 magnets
BF
BD
Red areas show m0H < -1.5T,
yellow -1.5 < m0H < -1.0T, etc.
Stripes are 0.1T intervals.
Looks like worst reverse flux value is around -2.3T, knee is -2.7T, likely OK without radiation but not much margin.

## Slide 42: Demagnetisation in new magnets
BF
BD
Could make the “high field” wedge at the end out of a different material grade, or SmCo

## Slide 43: 50% gradient / large clearance
BF
BD
Very similar, scaled up 2x

## Slide 44: All Magnets for 5+3 FFA1 and FFA2
BF
BD
FFA1
FFA2
FFA2 magnets scaled to 50% gradient, FFA1 at 100% (aperture already large)
96.9cm2
107.1cm2
72.8cm2
78.7cm2
All gradients between 35T/m and 43T/m
10cm

## Slide 45: Summary (updated magnets)
Reduced peak field allows larger apertures
  Easier to fit vacuum chamber and beam through
    The 10mm-to-magnet should give 7-8mm to pipe
What height should the synchrotron radiation slot be?
  E.g. 8mm full height minus both sides of chamber
  When known, can optimise lattice gradient
    Scaling law independent of maximum field, SR etc.
LDRD funding from Oct 2021  prototypes