## Slide 1: Fixed-Field Accelerators with Fixed Tunes… AND good Magnetic Efficiency
Electromagnets for FETS-FFA-like machine (3-12MeV protons)
Permanent magnets for Trbojevic proton therapy accelerator

## Slide 2: Introduction
Recent studies by Dejan Trbojevic have confirmed that non-scaling FFAs can have their tune dependence on momentum flattened by adding non-linear components to the magnet fields, although not necessarily for an unlimited momentum range.
Quadrupole affects tune level, sextupole affects dQ/dp, octupole affects d2Q/dp2, etc.

## Slide 3: FETS-FFA requirements
3-12MeV protons
4m average radius
Several 1m drifts (one per cell here)
Fixed tunes: DQx,y<0.01 in ring, <0.001 per cell
Qx,y tunable over full range of 1 in ring
  For exploration of the tune plane in R&D
  I chose 12 cells so this is 1/12 range per cell
Geometrical aperture 1250mm.mrad (large)

## Slide 4: Algorithm
Runge-Kutta 4th order tracking step
Loop to get trajectory in cell
Finite difference to get transfer matrix
  Also gives tunes if orbit is closed
Iterate (Newton) to find closed orbit
Loop over all FFA energies
Finite difference parameters to get response matrix of tune functions to multipole changes
Iterate (optimiser) to find fixed-tune lattice
Muon1
Muon1 cell optics mode
Muon1 FFA optics mode
Fixed-tune FFA optimiser
(parallel)

## Slide 5: Field Model
Midplane field is product of:
  Transverse polynomial up to dodecapole
    Rough initial field coefficients up to octupole were found by Muon1 genetic algorithm before using fixed-tune FFA optimiser
  Longitudinal integral of Gaussian at both ends
    Fringe length given by s=6cm
Off-midplane fields extrapolated by repeated derivatives of this product of three functions

## Slide 6: Fixed-Tune Cell Orbits
Target cell tunes Qx=0.216, Qy=0.213

## Slide 7: Fixed-Tune Cell Fields
F field +0.15 to -0.43T, D field -0.42 to -0.02T

## Slide 8: Cell Tunes
Target cell tunes Qx=0.216, Qy=0.213

## Slide 9: Field Profiles
Only plotted in beam region, including sagitta
3MeV, ring inside 
 12MeV, ring outside

## Slide 10: Field vs. Kinetic Energy

## Slide 11: Field vs. Momentum
Average field should be proportional to momentum
Not exactly because I used “average” position in each magnet

## Slide 12: Gradient vs. Momentum
In a thin-lens model, the gradients should be proportional to momentum
Here they are not, I suspect edge focussing

## Slide 13: Tunes Beyond Energy Range
Target cell tunes Qx=0.216, Qy=0.213
Hits magnet bounding box

## Slide 14: Orbits Beyond Energy Range

## Slide 15: Beta x,y vs. Kinetic Energy

## Slide 16: Tune Range Requirement
Qx,y tunable over full range of 1 in ring
  For exploration of the tune plane in R&D
  I chose 12 cells so this is 1/12 range per cell
Qx=0.216, Qy=0.213 would be ring tune of (2.592,2.556)
So choose 2.5 to 3.5 ring tune range in both planes
  0.2083 to 0.2917 cell tune (all combinations)

## Slide 17: Four Tune “Corners”
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 18: Cell Tunes at Corners
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 19: Cell Tunes at Corners (zoom)
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 20: Field Profiles of Corner Designs
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 21: Designs Summary Table
Cell Qx | Cell Qy | Max tune error | Max field (T) | Orbit range (m)
0.2083 | 0.2083 | 0.00074 | 0.5204 | 0.641
0.2083 | 0.2917 | 0.00185 | 0.6128 | 0.688
0.2917 | 0.2083 | 0.00168 | 0.4466 | 0.389
0.2917 | 0.2917 | 0.00037 | 0.4004 | 0.381
0.216 | 0.213 | 0.00126 | 0.4310 | 0.573
Qx low, Qy high corner is most “unnatural”
  Largest orbit excursion, highest field
    Had to let optimiser vary dipole to stay in magnet box
Higher Qx tunes greatly improve orbit range

## Slide 22: Half-way Interpolation Result
What happens if you average the fields (equivalently, multipole coefficients) between two of the corner designs?
  (0.2917,0.2083),(0.2917,0.2917)  (0.2917,0.25)?
Not so bad, especially at higher energies, but needs re-tuning iteration

## Slide 23: Horizontal Omni-Magnets
“Arbitrarily” configurable field By(x)
  Are their own correctors
Try flat 80cm-wide poles, 8cm full gap, with large embedded pole face windings
  20 windings each top and bottom
  2x4cm cross-section, 4cm horizontal pitch
Main 8x16cm H-magnet-style coil for dipole
Pole face windings return on nearest side
  Produce quadrupole if all have equal current
Round ones were described in my IPAC’13 paper

## Slide 24: Main Dipole Coil @ 5A/mm2
Roughly flat field, about 0.4T
2D designs in Poisson/SuperFish
(plots are in cm, Gauss)

## Slide 25: Single Pole Winding @ 5A/mm2
Produces ~0.1T field plateau to return side

## Slide 26: Qx=0.2083, Qy=0.2917 F magnet
0.613T peak field, “hardest case”

## Slide 27: Qx=0.2083, Qy=0.2917 F magnet
Winding current densities were found by SVD / least squares

## Slide 28: Qx=0.2917, Qy=0.2917 D magnet
0.404T peak field, only requires small part of aperture

## Slide 29: Qx=0.2917, Qy=0.2917 D magnet
SVD only activates coils in the region they have an effect

## Slide 30: Magnets Summary Table
Cell Qx | Cell Qy | Magnet name | Max current density (A/mm2) | Max By error (G) | Max field (T) | Orbit range (m)
0.2083 | 0.2083 | F | 2.090 | 2.25 | 0.5201 | 0.641
 |  | D | 3.111 | 1.98 | 0.3921 | 0.460
0.2083 | 0.2917 | F | 3.056 | 3.31 | 0.6126 | 0.688
 |  | D | 2.955 | 2.31 | 0.4260 | 0.471
0.2917 | 0.2083 | F | 3.073 | 2.23 | 0.4418 | 0.389
 |  | D | 3.189 | 1.89 | 0.3370 | 0.247
0.2917 | 0.2917 | F | 3.480 | 2.50 | 0.3883 | 0.381
 |  | D | 3.944 | 2.58 | 0.4035 | 0.224
0.216 | 0.213 | F | 2.372 | 1.88 | 0.4224 | 0.573
 |  | D | 4.256 | 2.32 | 0.4270 | 0.400

## Slide 31: Quick Dynamic Aperture Test
Started 8 particles at (x,y) = (±2.5/0,±2.5/0)cm
  Cell Qx=0.216, Qy=0.213 design
Tracked in ring for 60ms, all survived
Some particles at 3cm did not
Can use e = xinj2/binj to get apertures
Energy | Cells (in 60ms) | Turns | ex (geom.) | ey (geom.)
3MeV | 697 | 58 | 471 | 428 mm.mrad
6MeV | 954 | 79 | 408 | 374 mm.mrad
12MeV | 1266 | 105 | 381 | 365 mm.mrad

## Slide 32: Dynamic Aperture Notes
FETS-FFA request was 100mm.mrad normalised at 3MeV (bg=0.080)
  = 1250 mm.mrad geometric
by = 1.46m at 3MeV injection point
  Implies y = ±4.27cm (or ±5.31cm at maximum by)
  Larger than the magnet aperture (±4cm)!
This DA is not the painted beam size, it is a stability margin (all beam ≤ 250 mm.mrad)

## Slide 33: Conclusion (part 1)
Found fixed tune lattices to ~0.001 in cell tune
  And automated: eliminated most hand-tuning!
Dynamic aperture low by factor 2-3× in e
  Not small by most standards: >400mm.mrad
  Haven’t explored the full tune plane yet
Magnetic efficiency about twice as good as (spiral) scaling FFA, magnets buildable
  ~0.6T max field on beam vs. ~1.2T
Very interesting machine type

## Slide 34: Future Work (still haven’t done!)
Dynamic aperture search of tune plane
  And maybe other parameters like fringe length or magnet edge angles (rect vs. sector etc.)
Try expressing transverse field as something better-conditioned than polynomials
  Like Fourier series, or Chebyshev polynomials
Maybe investigate low-level tune “noise” in Muon1 tracking/optics algorithm
  Could also be field model nonsmoothness

## Slide 35: Permanent Magnets for Hadron Therapy Accelerator

## Slide 36: Application
Dejan Trbojevic proposes to accelerate protons with a rapid cycle (100s of Hz to kHz) for FLASH hadron therapy
  Many machine cycles within 100ms allow different energy (depth) slices to be done as well as being quick enough to trigger the biological FLASH effect
Need an FFA ring which also has fixed tunes
  But needs to fit in the hospital, so smaller than a scaling FFA  nonlinear fixed-tune NS-FFA

## Slide 37: ‘FLASH’ Proton Therapy facility: Stony Brook University Hospital – Radiation Oncology
6. D. Trbojevic, Title: “Non-scaling fixed field alternating gradient permanent magnet cancer therapy accelerator”, patent number: US 9661737 B2, Date of the patent: May 23, 2017 (belongs to the DOE). https://patentimages.storage.googleapis.com/42/5e/92/f7da1cf617d6e3/US9661737.pdf

## Slide 38: Fast Cycling Synchrotron Cycles
t(ms)
Kinetic
Energy
250
(MeV)
16.5-30
One synchrotron cycle
Ex.1
Ex.3
Ex.2
Injection
Energy
Second synchrotron cycle
0.8ms < t < 1.85ms
1.3kHz< f < 540 Hz
RF manipulation
Extraction #2
Time of bunch flight 405-550 ns
At the injection porch time of 926 ms there are 1680 turns. 15 turns for 15 Cyclotron bunches and 1650 turns for RF manipulations
Injection
Porch
If the RF kicks are 30 kV, during the slip-stacking merge a difference in the time of flight for two 2 energies is 773ps. If the batches are 15 m apart it would take 370 turns to get them aligned. Next step would be to merge into one bucket by snaping the new RF voltage on.
Extraction kicker wave forms

## Slide 39: Fast Cycling Acceleration with Ferrite cavities
 | Choices for injector cyclotron |  |  |  | Units
 | ACSI | GE | TR-19 | IBA | 
Energy of Injector Cyclotron | 14 | 16.5 | 19 | 30 | MeV
Cyclotron current | 400 | 200 | 400 | 1200 | mA
Treatment charge | 60 | 60 | 60 | 60 | nC
Injection turns | 4 | 4 | 4 | 2 | #
RF acceleration per turn | 29.70 | 29.70 | 29.70 | 44.55 | kV
Calculation | Treatments Options |  |  |  | 
Turn duration | 585.74 | 540.6 | 504.8 | 405.1 | ns
Charge per turn | 0.234 | 0.108 | 0.151 | 0.486 | nC
Charge per injection | 0.937 | 0.432 | 0.606 | 0.972 | nC
Machine cycles | 65 | 139 | 100 | 62 | #
Machine cycle rate | 540 | 540 | 540 | 809.95 | Hz
Outputs |  |  |  |  | 
Treatment time | 120 | 257 | 185 | 76.54 | ms
By Stephen Brooks

## Slide 40
Matching of the Multiple Energy Orbits to the Straight Section
5.8 m

## Slide 41: Lattice Converted from BMAD
Multipoles dipole…dodeca
Three cells for field wrap
This worked well in BMAD, fixed stable tunes from 10MeV – 250MeV

## Slide 42: BMAD and Muon1 Magnet Models
BMAD has a zero-length end field model
Muon1 has a Maxwellian fringe field model with finite length
  But you have to choose the length yourself!
We also changed from sectors to rectangles but that turned out to be a small effect
Discrepancy shown here is probably because BMAD end fields were accidentally turned off!

## Slide 43: Field Profiles

## Slide 44: Original Lattice in Muon1
It’s unstable at the low end no matter what fringe field length I choose
MeV
Cell tune

## Slide 45: cos(cell tunes)
Even with a fringe=1mm it is unstable, although closed orbits exist
MeV

## Slide 46: Peak Fields on Orbit (vs. Energy)
MeV
T

## Slide 47: This cell can be easily fixed using the same Algorithm
Runge-Kutta 4th order tracking step
Loop to get trajectory in cell
Finite difference to get transfer matrix
  Also gives tunes if orbit is closed
Iterate (Newton) to find closed orbit
Loop over all FFA energies
Finite difference parameters to get response matrix of tune functions to multipole changes
Iterate (optimiser) to find fixed-tune lattice
Muon1
Muon1 cell optics mode
Muon1 FFA optics mode
Fixed-tune FFA optimiser
(parallel)

## Slide 48: Tunes After Correction in Muon1
MeV
Cell tune
Tunes stable from 10MeV – 250MeV and somewhat constant, although could be improved.
(Wiggly near low energy end because rigidity changes fast there).
Qx = 0.1547 ± 0.0013
Qy = 0.0571 ± 0.0034

## Slide 49: Field Profiles After Correction

## Slide 50: Peak Fields After Correction
MeV
T

## Slide 51: Orbits and Fields in Muon1

## Slide 52: Increase Low Energy to 16.5MeV
Use a bigger cyclotron as an injector
  Momentum ratio 5.31×  4.13×, easier to do
Tunes a little better but still wiggly
Qx = 0.1547 ± 0.0008
Qy = 0.0581 ± 0.0031

## Slide 53: Allow 14- and 16-pole Components
That’s noticably better (2-3× less variation)
Probably polynomial isn’t the best field basis
  Use Fourier series transversely instead?
Qx = 0.1545 ± 0.0004
Qy = 0.0577 ± 0.0010

## Slide 54: Field Profiles 12- vs. 16-pole
About 1 part in 1000 change

## Slide 55: Orbits and Fields in Muon1

## Slide 56: Permanent Magnet Designs (F)
cm grid
NdFeB material
N42EH grade
Br=1.3T
107.28cm2 area
64.4 x 16mm aperture
Good field X±26.2mm
1.88T max field

## Slide 57: Permanent Magnet Designs (D)
cm grid
NdFeB material
N42EH grade
Br=1.3T
119.39cm2 area
51.8 x 16mm aperture
Good field X±19.9mm
1.85T max field

## Slide 58: Magnet Field Error Graph (F)
~2×10-4 relative error

## Slide 59: Magnet Field Error Graph (D)
~1×10-4 relative error

## Slide 60: Permanent Magnet Wedges
We bought enough wedges to make two 45mm test sections of the nonlinear D magnet

## Slide 61: Conclusion (part 2)
It looks like permanent magnets with small apertures and >1.8T fields can be used as a driver for FLASH proton therapy
  No open midplane needed for protons
  Higher field gives more compact machine
Main challenge is actually RF that sweeps frequency at ~500Hz
  Have had some initial discussions with RAL
  May be similar to 2RF or PAMELA RF study