## Slide 1: Ultra-low Emittance Bunches from Laser Cooled Ion Traps for Intense Focal Points

## Slide 2: Ion Traps & Laser Doppler Cooling
Paul trap configuration has four AC transverse electrodes (like alternating gradient focussing) and DC longitudinal end caps
Temperature limit TD = ℏG/2kB = 0.552mK
Transverse trap electrodes
Longitudinal trap electrodes with injection / extraction hole
Ions
Laser
40Ca+
397nm photon
Emitted in random direction
Linewidth G = 2p*23MHz, frequency f = c/397e-9 = 755THz
Active over velocity range ~ c(23MHz/755THz) = 9.1m/s
Tune so that force pushes more on ions moving towards laser

## Slide 3: S-POD, IBEX experiments
Fluorescence of Coulomb crystal in S-POD trap, from K. Izawa et al., J. Phys. Soc. Jpn., Vol. 79, No. 12 (U.Hiroshima)
The IBEX Paul trap (RAL) with vacuum chamber opened. The four rods in the center of the image are the transverse trap electrodes.

## Slide 4: Laser Doppler Cooling Simulation

## Slide 5: Laser Doppler Cooling Simulation
N = 500 ions

## Slide 6: Ion Trap Flexibility
Flexible source with variable parameters over wide range:
  Bunch charge (1 to 107 ions)
    Via gas pressure, trap voltage
  Bunch size, aspect ratio, shape
    Via trap voltages, trap geometry, collimation
  Emittance/temperature
    Stop cooling part way, or tighten trap ( quantum limit!)
  Ion species
    Use sympathetic cooling - mix coolable ion e.g. 40Ca+ ion in contact with desired species
  Easily exchangeable electrode configurations
enorm,rms ≥ ℏ/2mc
Muroo et al., PTEP2023 063G01
IBEX 106-107
Martin et al., New J. Phys. 21 (2019) 053023
Takai et al., Japan. J. Appl. Phys. 45, No. 6A (2006) 5332-5343
S-POD 1-107

## Slide 7: Flexibility e.g.: 2D Coulomb Crystal
Made the transverse trapping voltages much smaller than the longitudinal

## Slide 8: What do we do with this beam?
x
p or gv
Typical ion source beam
x
p or gv
Parameter | Ion source | Ion trap
N | 109 | 500
enorm,rms | 10-7m | 2×10-13m
sx | 1mm | 90mm
sv | 30km/s | 0.65m/s
T | 4.3MK | 2mK
Parameter | Ion source | Ion trap
N | 109 | 500
enorm,rms | 10-7m | 2×10-13m
s*x | 9.4nm | 18fm
s*q | 10mrad | 10mrad
L/bunch | 9×1028cm-2 | 6×1027cm-2
Accelerate to
1000GeV/u
Focus with
sp/p = s*q = 0.01
Ion trap beam

## Slide 9: High Specific Luminosity Scaling
Luminosity is held constant if N ∝ s*
  If s*q is also held constant, that’s N ∝ s* ∝ e
But luminosity per ion increases at smaller N
  6×1027cm-2 from 2×500 ions is 130,000 times more efficient than 9×1028cm-2 from 2×109 ions
In fact the ion trap saturated the cross section
  If stot > 84mbarn, then >500 collisions expected
  One pass and it’s gone!

## Slide 10: What’s going on in the longitudinal plane? and Other Questions
Need short bunch length for good collisions
  The ion trap’s emittance is small in all three planes
The bunch seems pretty “opaque”, does it self-interact?
  Space charge repulsion prior to the focus?
Why don’t collider interaction points create a sharp focus all three space planes?
  Is that even possible?
    Yes, but relativity reduces longitudinal Dvbunch rest frame

## Slide 11: Bunch Implosion Radius Limits
Model: imploding uniform sphere of charge in the bunch’s rest frame
Space charge dictates r ≥ 1/(4pe0) Nq2/Ek,in
  Ek,in is inward kinetic energy at sphere surface
  Density r ∝ N/r3 ∝ Ek,in3/N2
Emittance dictates sx ≥ enorm,rms/sbg
  sx = r/sqrt(5), sbg = (bg)in/sqrt(5)
sbg,Transv. = (bg)beams*q, sbg,Long. = bbeamsp/p

## Slide 12: Minor Complexities
Ca+ will behave as Ca20+ once nuclei are within each others’ electron clouds (no shielding)
Space charge forces for a non-spherical uniform charge density ellipsoid are actually coupled between the planes (but still linear)
  Just like the 2D KV envelope space charge force
  Integrated backwards from focal point and fitted focal ellipsoid size to match incoming s*q and sp/p

## Slide 13: Energy Scaling Graph
For N = 500 ions
sp/p = s*q = 0.01
Nuclear density 2.5e17
Water 1e3
Doesn’t quite get there, mainly because of longitudinal plane
Switch to using fully-stripped ion charge when orbitals touch

## Slide 14: Energy Scaling Graph
For N = 500 ions
sp/p = s*q = 0.02
eL = 1.9eT
Can fix by using a tighter ion trap with ~20× smaller emittance (not too hard) and 2× larger dp/p (helps a lot).
Colliding bunches could also work, as might an FFA channel supporting a wider dp/p.
Nuclear density 2.5e17
Water 1e3

## Slide 15: Potential Future Applications
We can already accurately position objects close to the nuclear size (e.g. LIGO mirrors)
The low emittance (entropy) of the ion trap initial state allows nuclei to be placed in particular locations deliberately, e.g.:
  Make white dwarf, neutron star matter
  3-way and multi-way particle collisions
  Synthesise custom shapes of nuclear matter
  Possible neutron-rich superheavy elements

## Slide 16: What can stop us?
Space charge, emittance and energy spread considerations as mentioned previously
Optical aberrations!
  Lenses are not linear, spherical aberration, chromaticity etc.
Can focussing in all three planes be done?
Experimental noise, jitter etc.
  Ideas for feedback using scattered pattern from interaction point
    Coulomb scattering has very good resolution

## Slide 17: Focussing Beamline Simulation
Test of three-plane focusing and optical aberration correction (at lower energy)
  Input N=20000, T=2mK ion trap bunch parameters
  Given energy chirp
Curved electrostatic beamline
  Point-source ‘electrodes’
    Arranged in rings of 12
    Generalised multipole lenses
Goal: minimise 3D focal size

## Slide 18: Focussing Beamline Simulation

## Slide 19: Optimisation of Electrode Voltages
11 electrode charges were optimised per electrode ring (12 minus one monopole)
The bunch initial chirp was also optimised
So 15 electrode rings  166 parameters
Used modified Levenburg-Marquardt method with nonlinearity correction
  See https://arxiv.org/abs/2307.03820
    Response matrix  SVD  try various damped inverses
    Sample additional points to infer nonlinear behaviour

## Slide 20: Improved L-M Optimiser

## Slide 21: Focal Point Optimisation (T=2mK)

## Slide 22: Focal Point Optimisation (T=0)

## Slide 23: Focal Size vs. Electrodes Used
T=0 line shows limit from pure aberrations
Lines are limited by normalised emittance (const.) and chosen dp/p chirp (generally increasing)
Numerical accuracy floor?
“Theory” is the minimum allowed size taking account the emittance and chirp

## Slide 24: Focal Size vs. Energy
Beamlines with only one electrode ring stop here
Focal sizes plotted for all numbers of electrode rings
Two rings here
Higher energies don’t use 1% dp/p, could need more electrode rings or just be hitting numerical noise

## Slide 25: Optimal Chirp vs. Electrodes Used
As more beamline elements are allowed, optimiser can cancel aberrations for a larger momentum range
Higher energies have smaller geometrical emittance already, less incentive to increase dp/p

## Slide 26: Focal Size vs. Initial Chirp
Scalings as expected, ignoring 1TV that has a bit of trouble

## Slide 27: Cooling at High Energy?
Doppler cooling also works in a boosted frame
Pros:
  Can create cold beams at or near final energy
    Bypass jitter from RF and acceleration process
  Use blue-shift to cool using harder transitions(?)
Cons:
  Needs a low-intra-beam-scattering (IBS) ring lattice
    Very low phase advance per cell
    Bunch velocity distribution near-Maxwellian
  Too much energy or field could strip ions
  Ring is more expensive than an at-rest ion trap
PALLAS ring did this, but beam velocity only 2.8km/s
Schramm et al., Plasma Phys. Control. Fusion 44 (2002) B375–B387
Improves cooling rate, but increases limiting temperature

## Slide 28: Increasing Current Throughput
Throughput of basic trap isn’t great
  107 ions every 16ms (62.5Hz) is 100pA average
But trap is small enough and 10ms is short enough that could make a CW cooling channel at a PALLAS-like speed of 50km/s
  Bunches every 100ns (10MHz), spaced by 5mm
    Average current could go as high as 16uA
  Length of channel 16ms*50km/s = 800m
    Could coil it up, trap can be narrow, rods few mm apart

## Slide 29: Recent Funding at BNL
Received Lab-Directed R&D (LDRD) funding at BNL, total $400k over 2 years, Oct ‘23-Sep ’25
Proposed to “construct a basic foundational system”
Probably without laser cooling to start with

## Slide 30: Conclusion
Ultra-low emittance bunches provide some interesting unexplored regimes
  106 times smaller emittance vs. conventional bunches
  Extraction into an accelerator would be new
Lower entropy initial states are going to be the long term trend as experiments improve
Can even achieve the quantum ground state
  Produce e.g. entangled spin states in a beam!
Ultimately, appears capable of custom synthesis of nuclear density matter

## Slide 31: Beam sizes in focussing channel

## Slide 32: Doppler-cooled rings as of 2014
Noda et al., IPAC2014