## Slide 1: Results from the ATF FFAG experiment
Only 36, 54MeV done so far
18, 24, 72MeV still to-do

## Slide 2: Outline of Main Components
ATF beam pipe
1” diam.
2” diam.
Flexible bellows and flange size adapter
FFAG pipe through magnets
Fixed table
Movable table
Beam screen (FFAG) and camera
Beam stop
Injection X position and angle adjustment
Beam direction
Screen (POP11)
Screen (POP10)
Triplet
Steerer (GT7)
Steerer (GT3)
For each energy, do 2D steerer current scans
  GT3X, GT7X (x,x’)
  GT3Y, GT7Y (y,y’)
  GT7X, GT7Y (x,y)
Plus four larger-range 1D scans and a quad scan of the triplet

## Slide 3: Tracking of (x,x’) Offsets
Trajectories have been magnified transversely by 16x for visibility
xin ±1mm
x’in ±10mrad

## Slide 4: NS-FFAG Beamline Parameters
Parameter | Value | Units
Particle species | Electron | 
Energy range | 18-72 | MeV
Cell Length | 0.234301 | m
Cell Angle | 6.666… | degrees (54 per turn)
R = avg. radius of curvature | 2.01367 | m
Max orbit excursion | 18.21 | mm (from circle radius R)
Tune range per cell | Qy,72 = 0.029, Qx,18 = 0.411 | cycles
Cell lattice | halfD2, QF, D1, BD, halfD2 | 
Drift lengths | D1 = 57.35, D2 = 57.65 | mm
Number of cells | 6 | 
Total length | 1.40581 | m
Total angle | 40 | degrees

## Slide 5: Matched Orbits through Fieldmaps
18, 24, 36, 54, 72MeV

## Slide 6: Beams Exit from Periodic Cell

## Slide 7: Magnet Design and Parameters
Parameter | “QF” magnet | “BD” magnet | Units
Length | 57.44 | 61.86 | mm
Dipole By(x=0) | 0 | -0.37679 | T
Quadrupole dBy/dx | -23.624 | 19.119 | T/m
Inner radius (magnet pieces) | 37.20 | 30.70 | mm
(shim holder) | 34.70 | 27.60 | mm
“Pole-tip” field (magnet pieces) | 0.879 | (-)0.964 | T
Outer radius (magnet pieces) | 62.45 | 59.43 | mm
(tubular support) | 76.2 | 76.2 | mm
QF
BD

## Slide 8
All the magnets had already been built as part of CBETA R&D and all have had iron wires inserted.

## Slide 9: Radii/Clearances
 | Radius wrt torus (mm) | Distance to previous (mm)
Maximum beam excursion | 18.21 | 
Vacuum pipe inside | 23.75 | 5.54 (12.00 in CBETA)
Vacuum pipe outside | 25.40 | 1.65 (pipe thickness)
Shim holder inside (BD) | 27.45 (27.60 straight) | 2.05 (air gap)
PM block inside edges (BD) | 30.55 (30.70 straight) | 3.10 (shim holder)
May have been a bit over-optimistic with beam clearance, seeing scraping near 36MeV
Re-aligned pipe recently because it was being pulled off-centre by bellows

## Slide 10: Girder and Supports Construction
Feb 22, 2017

## Slide 11: Detail: Magnets on the Girder
Apr 7, 2017

## Slide 12: Pipe undergoing Leak Check
Apr 14, 2017

## Slide 13: Picture of Everyone Standing By It
ATF experiment AE79
May 1, 2017

## Slide 14: First Beam during Fault Studies
May 4, 2017
54MeV was the first energy to be tested

## Slide 15: With Survey “Faro Arm” Attached
May 5, 2017
Most magnet offsets <0.2mm; RMS 0.1mm or better

## Slide 16: Beam X,Y Scan at 54MeV
May 8-9, 2017
Tracking model:
Qx = 0.119
Qy = 0.055
6Qx = 0.713
6Qy = 0.329
More analysis to do later
Each setting in the 2D current scan is given a colour and all the 11*11 beams at each diagnostic overlayed

## Slide 17: Input/Output Position at 54MeV

## Slide 18: Beam X,Y Scan at 36MeV
May 11-12, 2017
Tracking model:
Qx = 0.176
Qy = 0.122
6Qx = 1.056
6Qy = 0.734
More analysis to do later
Here we encountered beam scraping quite close (~2mm away) to the nominal closed orbit

## Slide 19: Input/Output Position at 36MeV

## Slide 20: Conclusion & Future Plans
Beam has turned a nontrivial angle (40°) in six cells of a non-scaling FFAG, at 36 and 54MeV
  No highly nonlinear aberrations seen
Will do other energies in June and July
  Have to give diagnostic back to RHIC by August
Table is currently aligned to 72MeV position
New pipe restraint near bellows
Pipe realigned to be better centered

## Slide 21: Source Code